TECHNICAL SPECIFICATIONS

and

OTHER REQUIREMENTS/CONDITIONS

Subject of contract

The subject-matter of this contract is procurement of new or refurbished, eventually, demonstration hybrid equipment for high resolution exposure of thermal print plates (CToP).

Required technical specification of the equipment:

Hybrid equipment that can be used for high resolution exposure of offset print, but also nyloprint printing plates (10.160 dpi) and DITR or LADF films.

We assume that this equipment shall be capable of exposing print plates for the following print techniques:

- water offset printing plates (for example, Kodak DITP Gold)

- waterless offset printing plates (for example Toray Waterless TAC VG5)

- poly template plates for Intaglio thickness 2.3 mm (for example, Nyloprint Digital WS230SD)

- nyloprint letterpress print plates thickness 0,73mm (for example, Nyloprint Digital WS73D)

- flexotisk print plates

and shall also be capable of exposing (DITR/LADF 0175) film to the extent of the formats and thicknesses stated below.

|  | Machine | Format (mm) | Technology | Force (mm) | Registration system |
| --- | --- | --- | --- | --- | --- |
| Printing plates | GTO | 510 X 400 | AL plates | 0.15 | BACHER |
|  | KBA | 743 x 557 | AL plates | 0.30 | BACHER 2002 |
|  | KBA |  | NYLOPRINT | 0.73 | BACHER 2002 |
|  | Printing machine B1 | 1060 x 795-820 | AL plates | 0.30 | BACHER 2000 |
|  | Printing machine B1 | 1060 x 795-820 | NYLOPRINT | 0.73 | BACHER 2000 |
|  | Rotary press | 510 x 650 | AL plates | 0.30 | BACHER 2002 |
|  | Rotary press | 510 x 650 | NYLOPRINT | 0.73 | BACHER 2002 |
|  | Simultan II | 760 x 648 | NYLOPRINT | 0.73 | KBA Intaglio Color 8 |
|  |  | 750 x 617 | NYLOPRINT | 2.30 | KBA |
| Film | for NYLOPRINT | 1060 x 820 | negative/diapositive |  |  |
|  | screen printing | max 700 x 500 | diapositive |  |  |
|  | screen printing card VZ II | max 330 x 450 | diapositive |  |  |
|  | minting | max 800 x 570 | diapositive |  |  |

Required technical parameters of the equipment:

Resolution:					10160 dpi

Thickness of offset printing plates:		0.15 mm and 0.28-0.30 mm

Thickness of nyloprint printing plates:	0.73 mm and 2.3 mm

Dot size:			 		max. 5μm

Repeatability:					max. ± 0.01 mm

Precision:			 		max. ± 0.02 mm

Machine dimensions and weight:		see below in the assignment

Input data:					1 bit TIFF format

Required compatibility:			RIP Prinergy Connect Rtpo

GS Layout Plus / Corwina

Other arrangements, terms and conditions are specified in the purchase contract, which comprises Annex 2 and is an integral part of the tender documentation (hereinafter the “TD”).

Other requirements for the equipment and its delivery:

- After installation of the equipment and training of the operating and maintenance personnel, a 30-day trial run of the equipment will commence.

- The consumables necessary for commissioning and testing of the equipment must be included in the price;

- Machine dimensions and weight:

With regard to the limited dimensions of the transport routes, the equipment must be supplied or adapted in such a manner that allows its transfer to the installation site, which is the existing space of “Copy room” in the 3rd floor (the floor plan of the room is shown in Annex 10 Floor plan with a plotted device). The Tenderer will have a possibility to get acquainted with the transport route before submission of the tender bid, see point 14 in the TD.

- draw the offered equipment in the enclosed floor plan and pass it on as:

•        Pdf or in printed form

•        Electronic form for CAD program

- Only quality components produced with high technical level worldwide may be used in the Device.

- Complete control of equipment (the control SW, descriptions of control elements) and a service menu according to the valid EU directives in Czech;

- Equipment labels must be in Czech or international symbols.

- The equipment must be installed in such a way that is operation complies with the technical 
and safety norms in force within the EU as well as the requirements of Czech standards applicable to its technical implementation and occupational safety according to the regulations in force at the time of delivery;

- The Tenderer shall provide the Contracting Authority with an indefinite, non-exclusive and, in case of resale, transferable right to use the computer software used for the subject matter of the public contract within the scope machine use for the agreed purpose (plates and films exposure). The contracting authority shall have a right to use all delivered software products in accordance with the copyright of the seller. However, the Contracting Authority is not allowed to interfere with the computer programs in any way or modify their functions;

- Undertaking on the part of the Tenderer that in the case of demonstration or refurbished equipment, the laser equipment will not have been in operation for more than 5,000 hours at the time of handover;

Time and place of delivery

# Delivery deadline: 	at the latest within 26 weeks of signature of the contract (6 months)

# Deadline for commissioning and handover for trial operations: 	at the latest within 26 weeks of signature of the contract

# Delivery/performance location:	STÁTNÍ TISKÁRNA CENIN, státní podnik

# Prague 1, Růžová 6, No. 943, 110 00, Czech epublic

# (2nd floor)

# Text boxes

Equipment for high resolution exposure of thermal printing plates

CToP