TECHNICAL SPECIFICATIONS

Main overhaul

spare parts and PLC and control console upgrade

push buttons, fuses, new sensor, overhaul of hydraulic

oscillation cylinder and overhaul of hydraulic pump

OVERHAUL IN STC (PRAGUE)

Complete Dismantling of all Aggregates

Installation of the Spare Parts

Final Assembly

Putting into Operation

Print Test

Site Acceptance Test (2 days - 8'000 s/h - 1 production shift / day)

DOCUMENTATION

New Documentation 2 copies in English

Documentation paper form and CD

SPARE PARTS

Feeder

Mabeg- Feeder

E-320

Sheet 2

Replacing of Pos. 14,15,16,21

Sheet 3

Replacing of Pos. 13,14,15,17

Sheet 5

Replacing of Pos. 40,41,44,45,46,47,50,51,52,53,54,55,55,56,57,60,62,63,64

Sheet 6

Replacing of Pos. 10

B+E- 295

New Sidelay Side I

Sheet Infeed

Group: 123

Replacing of Pos. 35,36,42,77,82

Group 125

Replacing of Pos. 22,38,47,48,49,53,57,67,73,92,95,100

Group 126

Replace of Pos. 04,09,13,14,15,17,18,27,32,34,42,46,50,55,56,57,58,59,60,61,62,65,74,76

Group 127

Replace of Pos. 04,09,10,25,34,41,51,61,62,86,94

Group 133

Replacing of Pos. 17,27,29,40,50,56,61,62,74

Group 135

Replacing of Pos. 39,41,43,45,65,66,67,68,69,70,71,74,75,84,89,93,106,109,110,116,121,122,130,144, 145

Group 152

Replacing of Pos. 11,16,20,23,25,26,27,28,32,41,42,43,46

Group 154

Replacing of Pos. 06,07,08,09,34,35

Group 155

Replacing of Pos. 01,02,05,06,07,08,17,033,34,38,39,41

Group: 156

Replacing of Pos. 06,15,20,21,34,38,47

Group 161

Replacing of Pos. 29

Group 162

Replace of Pos. 07,11,36,38,64,70,87

Printing Unit

Group 210

Replace of Pos. 16

Group 221

Replacing of Pos. 31,41,47,62,83

Group 244

Replacing of Pos. 60,78,138,139

Group 246

Replacing of Pos. 44,45,47,48,52

Group 260

Replacing of Pos. 11,12,16,20,23,24,25,26

Inking Unit Recto and Verso

Group 303

Replacing of Pos. 16,25,27

Group 333

Replacing of Pos. 32,34,35,44,45

Aditional only for one cylinder due to damage 13,22,36,48,53,66

Group 336

Replacing of Pos. 09,24,30,37,39,58,64

Group 339

Replacing of Pos. 41,63,73,74,75,76,78,79

Group 319

Replacing of Pos. 04,05,07,20,23,24,34,38,40,45,52,53,59,61,67,68,73

General

Overhaul of hydraulic pump.

Replacing of flexible hydraulic hoses Inking Units, Rotary Unions, New Motor for the Suction Roller Drive Delivery

Electric

Change of the existing control system T300 with T100 to the newest control system with Windows Control Console

Consists of:

Exchange of the control system T300 in the existing switch cabinet through the newest control system

Retrofit (exchange) of the redundancy control system T300 through the newest control system

Exchange of  control console VT100 through new Windows control console

Sinus Module

New Timing Unit

Spare parts

Documentation

Hardware, Software

Information

Control system exchange must corresponds to the safety standard to the year of the machine-production, with the innovation that the safety functions 2-channels are implemented.

That means, in the case of an error in the 1.Control system becomes the machine stopped by the 2. Control system.

The newest control system will guarantees that spare parts or compatible parts for this system are available for 10 years as starting from the signature of Handover protocol.

Control Console Single Desk

New main drive

Function

The Package Main Drive is the main drive for the complete machine .

Location

The package is located in the Switch Cabinet (Frequency Converter) and on the printing unit.

Parts

New Converter installed in the main switch cabinet..

New Main Motor with connection parts to the main drive shaft

Ultrasonic Double Sheet Detector

Function

The function is to detect double sheets which came from the feeder.

If the sensor recognize a double sheet then stops the sheet tranfser table and the sheet goes not in to the machine.

The printer has to remove the double-sheet.

Location

The Ultrasonic Double Sheet Detector is located in the aggregate Sheet Infeed between the sidelays.

Oscillation roller drive

Function

The Oscillation Roller Drive is a electronic component which controls the roller oscillation.

Location

The Drive is located in the inking units recto and verso.

Thermoregulation unit

Compact unit for the automatic temperature control of reciprocating distributor rollers of the machine.

The temperature is controlled by water circulation in two independent closed circuits, i.e.:

Inking unit recto

Inking unit verso

The unit must containing:

Water reservoir, capacity 200 litres, approx.

Automatic filling valve, safety valve and expansion vessel.

Heat exchanger for cooling in open circuit using water

Recycle pump between the tank and the heat exchanger for cooling.

2 thermoregulating modules, each consisting of:

circulating pump

3-way motorised valve

thermocouple

electric heater

flow indicator

air bleeder

Electric control cabinet equipped with some PLC suitable for the Arcnet communication with the console of the printing machine in case of remote installation of the unit.

Frontal panel equipped with Touch Screen for the control of the operation.

The supply must include:

Set of flexible hoses for connecting the printing machine  - (distance max.: 50 m)

50 kg of anticorrosive liquid to be introduced in the water reservoir.

Set of commissioning spare parts.

Requested technical data

Temperature of water in circulating circuits	adjustable from 20° to 90°C

Cold water requirement	max. 3000 l/h

Cold water pressure	> 2 bar

Loss of head inside the heat exchanger	100 kPa

Electrical feeding	3-phase AC 15 kW

Approx. weight in running condition	max. 1100 kg